First, this is one of the more dangerous tools in our space. It has a wide open area with horizontal spinning pieces and more than enough strength to pull you in or choke you to death if long hair is caught in it. There is a large red emergency stop button at waist height. This is designed to stop the machine automatically with your torso if you are pulled into it. Respect this machine or else.

- Keep long hair tied back and out of the way, wear short sleeves or sleeves should be rolled up.

- No gloves, necklaces, watches, rings, or other loose jewelry

- Always wear safety glasses

- Avoid reaching over the spinning chuck. For filing operations, hold the tang end of the file in your left hand so that your hand and arm are not above the spinning chuck.

- Keep your fingers clear of the rotating work and cutting tools. This sounds obvious, but don’t be tempted to break away metal spirals as they form at the cutting tool.

- Get in the habit of removing the chuck key immediately after use. Some shops recommend never removing your hand from the chuck key when it is in the chuck. The chuck key can be a lethal projectile if the lathe is started with it still in the chuck.

- Never use a file with a bare tang - the tang could be forced back into your wrist or palm. Inexpensive wooden handles are readily available for common file sizes and they can be made out of scrap wood easily.